| Roof Accessories TECHNICAL GUIDE | TG 07720 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Roof Scuttle Ladder Extension:

1.1.1	General:  Provide a ladder extension to facilitate access onto the roof after the roof scuttle is opened and back down the ladder upon leaving the roof.  Coordinate with TG 05510 - Metal Stairs and Ladders.

1.1.2	Use of “Safety Posts”:  Although extendable "safety posts" that can be attached to the ladder are available, their use is not recommended because of the difficultly in manipulating it to the extended and lowered positions while also holding onto the ladder.

2.	DESIGN ISSUES:

2.1	Roof Access:

2.1.1	Problem:  We have found that roofs which are inaccessible except through the use of special ladders, which the user does not need otherwise, are usually maintained infrequently, if at all. Such roofs cannot be expected to endure for more than a fraction of their normal life expectation.

2.1.2	Solution:  Accordingly, consider the following:

2.1.1.1	New and existing buildings: Scuttle access to the roof (including curbs, frame, access ladder, cover, etc.) is required on any building where a free-standing ladder more than 12' tall would be needed for someone to climb onto the roof deck.

2.1.1.2	For re-roofing projects: Where an existing scuttle opening is less than 2-1/2' x 3' and/or the scuttle frame is a "custom-made" one and/or is badly deteriorated, it should be replaced with a manufactured scuttle.

2.1.3	Other Considerations:  If the provision of a new or replacement scuttle for existing buildings is required based on the above criteria, confirm with The Project Coordinator and the Central Services Division (or other agency, as appropriate, with maintenance responsibility for the building) to decide whether the scuttle shall be included with the reroofing project.

3.	DRAWING NOTES: (Not Used)

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:  (Not Used)

6.	GUIDE SPECIFICATION:  (Not Used)

END OF SECTION 07720