| Fire and Smoke Protection TECHNICAL GUIDE | TG 07800 |
| --- | --- |

1.	COORDINATION ISSUES: (Not Used)

2.	DESIGN ISSUES:

2.1	Code Requirements: Properly address the code requirements for fire and smoke protection.

2.2	Draft Stops: Facilities having concealed attic spaces of combustible and non-combustible construction shall be provided with draft-stops where required by the Building Code.

2.3	Protection of penetrations through fire-rated walls and ceilings:  Penetrations through fire-rated walls and ceilings for equipment and fixtures (e.g. ductwork, outlet boxes, light fixtures, etc.) shall be designed and protected to maintain the integrity of the fire-rated assembly.  Ensure that fire/smoke dampers and firestopping dams and sealants are provided where required.  Where necessary, reference the applicable Underwriter's Laboratory (UL) assembly number.

2.4	Where attic spaces are required to be ventilated (wood or combustible construction unless the Building Official requires otherwise) ensure penetration through Fire Rated assemblies are protected.

3.	DRAWING NOTES:

3.1	Make it clean, visually and graphically on the plans and sections for the Contractor and DAGS Construction Administration Staff to locate the fire rated walls, ceilings and assemblies.

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:  (Not Used)

6.	GUIDE SPECIFICATION:  (Not Used)

END OF SECTION 07800