| Acoustical Tile Ceiling TECHNICAL GUIDE | TG 09510 |
| --- | --- |

1.	COORDINATION ISSUES:  (Not Used)

2.	DESIGN ISSUES: (Not Used)

3.	DRAWING NOTES:

3.1	Furring: Describe and show furring on drawings.  Use metal furring systems rather than wood.

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:

5.1	General:  This tech guide covers acoustical tiles fixed to a substrate and not suspended systems.

5.2	Submittals: Samples of the tile and any appurtenances together the manufacturer’s specifications of the tile and of the fastener system shall be submitted.

5.3	Flame Spread: Specify Flame Spread Class I, II or III as required to meet code requirements.  Check U.B.C. Chapter 8, INTERIOR FINISHES.

5.4	NRC Grade: Confirm the NRC (Noise Reduction Coefficient) grade to be used with The Project Coordinator and “DCC User’s Guides”.

5.5	High Humidity Locations: For high humidity locations, specify the proper acoustical tile to resist high humidity conditions.  Also, check the NRC range for this particular tile.

5.6	Fasteners: Fasteners shall be corrosion-resistant and of the type recommended by the acoustical tile manufacturer for the mounting.

5.7	Mounting: Screw direct to metal furring channels.

5.7.1	12 in. x 12 in. butt-jointed tile, attach with 3 fasteners along sides bearing on furring strips (6 total per piece).  12 inch x 24 inch butt-jointed tile, attach at corners and approximately 6 inches o.c. along furring strips (10 total per piece).

5.7.2	T & G tile, attach at both ends of transverse tongue and at approximately 6 inches o.c. along tongue bearing on furring strips.

5.7.3	Fasteners into the face of butt- jointed tile shall penetrate no more than 1/4 its thickness.  Those installed on T& G tile shall bear firmly against but not penetrate surface of flanges.

5.7.4	Acoustical tiles must be mechanically fastened to furring channels, and not directly to wood decking or other solid substrate.  Do not use adhesive mounting unless specifically approved by DAGS QC Branch.

5.7.5	Finish Work: Where used, plastic edge molding shall be positively secured to acoustical tile edges.

6.	GUIDE SPECIFICATION:   (Not Used)

END OF SECTION 09510