| Wood Flooring TECHNICAL GUIDE | TG 09640 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Make sure pH calcium chloride vapor moisture tests are conducted.

2.	DESIGN ISSUES:

2.1	Be aware that moisture or vapor transmission problems have occurred in projects with hardwood flooring.  Refer to TG 01450 Concrete Moisture Vapor Emission and Alkalinity Testing.

2.2	Consider using a commercial quality plastic laminate flooring system in lieu of a hardwood flooring system.  Confirm with Project Coordinator.

3.	DRAWING NOTES:   (Not Used)

4.	STANDARD DRAWINGS:    (Not Used)

5.	SPECIFICATION NOTES:

5.1	Gymnasium Hardwood (or Plastic Laminate) Flooring - Quality Assurance:

5.1.1	Problem:  Problems have been encountered where the project specifications required the contractor to have performed a minimum number of projects within a given time frame, in order to bid on a project. Examples of such problems would be where the contractor performed the required number of projects but the quality of the workmanship may have been unsatisfactory, or the quality of the work may have been acceptable but the required number of projects may not have been completed within the given time frame.

5.1.2	Solution:  Therefore, in order to promote competitive bidding and establish a degree of quality assurance, the paragraph in Part 6 shall be incorporated into the project specifications.

6.	GUIDE SPECIFICATION:

6.1	Gymnasium Hardwood (or Plastic Laminate) Flooring - Quality Assurance:

SPECIFIER’S NOTE:  The requirement that the Contractor be an approved installer of the proposed flooring manufacturer may be omitted where the work involves only refinishing and repainting of the wood flooring.

6.1.1	Contractor shall be experienced in the flooring field and approved as an installer by the proposed flooring manufacturer. Contractor shall be familiar with the proposed finish materials and experienced in their application.

6.1.2	Upon the request of the Contracting Officer, submit references and/or qualifications of past projects of similar magnitude and complexity.

END OF SECTION 09640