| Storage Shelving TECHNICAL | TG 10670 |
| --- | --- |

1.	COORDINATION ISSUES:

1.1	Contract Time:  Consultant shall account for required lead time when establishing the Contract Time in the Bidding Requirements.

2.	DESIGN ISSUES: (Not Used)

3.	DRAWING NOTES:

3.1	Unit Heights:  Indicate heights for all units on drawings, either plan or elevation.

3.2	Divider Shelves: Indicate extent and location on drawings, either plan or elevation.

4.	STANDARD DRAWINGS: (Not Used)

5.	SPECIFICATION NOTES:

5.1	Specification Paragraphs:  As of 03/2003, a complete Guide Specification for Storage Shelving is no longer being maintained by DAGS.  The Consultant shall utilize the following specification paragraphs and information as appropriate in the development of the Project Specifications.

6.	GUIDE SPECIFICATION:

6.1.1	Submittals (Part 1):   Submit 8 sets of shop drawings, color samples and manufacturer's literature for approval.

NOTES TO SPECIFIER:  Specify this type for Library Reading Rooms and Stack Rooms. Do not use for Storerooms.

6.1.2	Metal Bookshelving (Bracket Type) (Part 2):

6.1.2.1	General:

a.	Metal bookshelving: single face or double face, free-standing bracket type.

b.	Sheet steel:   cold-rolled furniture stock, gauges as specified.

c.	Assembly screws:  oval-head Phillips type stainless steel or pre-finished hot-dipped galvanized steel.

6.1.2.2	Upright Columns:  one-piece or two-piece channel shapes with stiffened flanges not less than 2 inches by 2 inches in cross dimensions, of 16-gauge material, with not less than 8 right angle bends, and of height shown on the plans.  Provide 2 rows of perforated slots on opposite sides spaced not more than 1/2 inch apart horizontally and exactly one inch o.c. vertically.

6.1.2.3	Base Brackets: 13-gauge material with vertical plates approximately 10 inches high, matching the shelving.  Extend in one piece, on both sides of the double-face units, to the opposite face.  Extend one inch to the rear of the uprights for the single-face units. Provide adjustable brackets which fit snugly around the upright to provide maximum support and safety. Bolt parts securely in a recessed manner.  Provide base plates which have a rubber pad to prevent lateral movement.

6.1.2.4	Bottom Channels:  one-piece, 20-gauge, 2 inches wide and formed to engage the base bracket and form a filler for the shelf back, allowing removal of any section.  Length: one section wide and not continuous.

6.1.2.5	Top Channels:  one piece, 18-gauge and 2-1/8 inch side to tie the upright. Attach to each upright with a bolt and an acorn-nut.

6.1.2.6	Bracing:  diagonal 1/4 inch diameter rod.   Install through the base assembly and the top channel, or between the uprights. Adjust by means of a nut or turnbuckle. Provide one pair of braces for not more than 9  feet of double-face shelving and an additional pair for every third additional section or fraction thereof.

6.1.2.7	Shelf Brackets for adjustable shelves:  16-gauge, same depth as the shelf and extending 6-1/4" above the shelf.  Roll front and top edges 1/4 inch continuously from the column to the bottom front edge of the bracket. Type:  J-fold to support full depth of shelf, with 2 hooks at the top and a lug at the bottom to prevent accidental dislodgement.

6.1.2.8	Adjustable Shelves:

a.	Construction:  one-piece, 18-gauge and 35-1/2 inches long between brackets, with three 90 degree bends box-formed to give a 13/16 inch face at front and back, and ends turned down 5/6 inch to engage brackets. Nominal depth: from center of column to face of shelf with actual depth one inch less than the nominal.   Design Load:  to support a uniform load of 40 pounds per square foot with a deflection of 3/16" or less. Nominal depth: 10 inches in Reading Rooms, 12 inches in Stack Rooms.

b.	Quantity:  Provide the following number of adjustable shelves for each 3-foot wide unit:

Unit			No. of Adjustable

Height			Shelves Required

42 inches			2

66 inches			4

78 inches			5

6.1.2.9	Base Shelf:   one piece 18-gauge and similar to the adjustable shelf and  including a base strip  with a one inch return top and bottom.  Attach shelf and base strip to the base brackets with concealed fasteners. Height of shelf and base:    3 to 4 inches.  Provide base shelf with a back to act as a rear book stop unless a separate book stop is available.  Provide a 1-1/2 inch by 3/8 inch ± sheet metal height adjustment strip (and attaching screws), as wide as and finished to match the shelving.

6.1.2.10End Panels:  one piece 18-gauge, installed at all exposed ends. Extend full width of the section, including the base, and full height. Configuration:  flush with a 3/4 inch radius return on the exposed edges. Provide return not less than 3 inches parallel to the face, with stiffener flanges at top and bottom. Overall thickness:   2 inches.

6.1.2.11	Finish and Color: Prepare each part for painting by a 5-stage cleaning and phosphatizing process known as Bonderizing. After passing through a dry-off oven, apply a finish coat of premium semi-gloss baking enamel and bake at high temperature.  Final finish thickness:  minimum 1.0 mil. Color:  one color as selected from the manufacturer's standard color chart by the Contracting Officer.

6.1.2.12	Canopy Top: Provide manufacturer’s standard canopy top for all units, including magazine racks.  Provide one piece 18-gauge tops for all units up to 42 inches high covering the area over the columns.

6.1.2.13	Closed Backs:  22-gauge steel punched on both vertical edges for bolting to upright columns.  Provide closed backs for single-face units not along wall.

6.1.2.14	Label Holders:   clip type to be secured to the face of the shelf without tools. Material:   aluminum or steel.  Furnish one holder for each adjustable shelf.

6.1.2.15	Book Supports:   wire book supports and hook-on book supports.

a.	Wire book supports:   stainless steel or prefinished galvanized steel, removable, adjustable and made for insertion into shelf flanges. Provide one for each adjustable shelf.

b.	Hook-on book supports:  9 inches high, 18-gauge, finish and color to match shelves. Provide one for each top shelf since wire book support cannot be inserted into canopy flange.  Provide buffer materials to prevent scraping at contact surface with shelf.

6.1.2.16	Rear Book Stop:  install on all standard adjustable shelves.  Book stops: 20 gauge, approximately 1/2 inch by 1-5/8 inch with four (4) 90 degree bends.  Hook book stops to the perforated slots of the upright columns.  Also install a rear book stop on the base shelf unless it has a back of its own.

6.1.2.17	Divider Shelves:  install on [Insert quantity] 3-foot unit of shelves.  Provide the same quantity of divider shelves of the same depth  as for one 3-foot unit of standard shelves. Provide 5 five 20-gauge steel dividers, 6-1/4 inches high for each divider shelf.

6.1.3	Magazine Racks (Part 2):  of the same material and construction as outlined above for the shelving. Provide units as shown on the drawings, approximately 36 inches wide by 42 inches high by 14 inches deep.  Provide 2 sloping shelves on each unit - one adjustable shelf and one base shelf.

NOTE TO SPECIFIER: Specify this type for storerooms only.

6.1.4	Metal Storage Shelving (Open-Type) (Part 2):  Heavy duty, free-standing type, of steel, meeting the following requirements:

6.1.4.1	Posts:  offset angle 14-gauge hot-or cold-rolled steel, minimum 1.875 inches by  1 inch and punched on 1-, 1-1/2- or 2-inch centers. Beaded or Delta posts, 14-gauge:  acceptable for front posts only. Where resilient flooring is used, attach a metal floor shoe or foot plate to the bottom of each post to transfer the post load to the floor without cutting into the flooring.  Where posts are anchored to walls, provide hardware and parts as necessary to enable height adjustment of front posts as necessary for full bearing.

6.1.4.2	Shelves:  18-gauge with two 90 degree bends along side edges to form a channel shape and three 90 degree bends along front and back edges to form an open-box shape.  Equip each shelf with 4 shelf hangers. Design Load:  to support a uniform load of 40 pounds per square foot with a deflection of 3/16 inch or less.

6.1.4.3	Cross-Braces:  1inch wide by 13-gauge thick steel attached to posts at 30 inches o.c. vertically, with one cross-brace at the back and one at each side.

NOTE TO SPECIFIER: Modify depth of shelf to suit your project.

6.1.4.4	Section Size:  84 inches high by [12] inches deep by 48 inches wide, with 7 shelves including the top and bottom.

6.1.4.5	Finish and Color:  Bonderized and finished with baked enamel. Color:   as selected by the Contracting Officer from manufacturer's standard color chart.

6.1.5	Installation (Part 3):   Where shelves are located against a wall, anchor each post to the wall using a clip angle primed and painted to match the shelving, bolted to the post with 1/4 inch bolts and fastened to the walls with anchors appropriate to the wall material. For metal bookshelving, move the height of the adjustment strip as necessary to cover the gap between the baseplate and floor due to any out-of-level condition of the latter. Where single-face shelves are free standing, provide horizontal steel braces primed and painted to match the shelving at the top of each post to tie the shelves to adjacent shelves or to the nearest wall.

END OF SECTION 10670