| Hazardous Material Remediation (Attachment B) TECHNICAL GUIDE | TG 13280 |
| --- | --- |

SUMMARY OF EPA INTERPRETATIVE RULE FOR ROOFING PROJECTS (40 CFR 61)

New APPENDIX A TO Subpart M - Interpretative Rule Governing Roof Removal Operations.

The following is a summary with paragraph and page numbers as used in the Interpretative Rule

Page

I.	Applicability of the Asbestos NESHAP						31158

1.1	Asbestos-containing material (ACM) is material containing more than 1% asbestos as determined using Polarized Light Microscopy.

ACM is classified as "friable" or "nonfriable".

Friable. When dry, can be crumbled, pulverized or reduced to powder by hand pressure.

Nonfriable. When dry, cannot be crumbled, pulverized or reduced to powder by hand pressure.

1.2	Nonfriable ACM is further classed as follows:			31158

Category I. Asbestos containing gaskets, packing, resilient floor covering, mastic, and asphalt roofing products (built up roofing, single-ply membrane systems, shingles, underlayment felts, roof coatings and mastics and base flashing).

Category II. All other nonfriable ACM including asbestos-cement shingles, tiles and boards. Generally speaking, Category II is more likely to become friable when damaged than is Category I.

Potential for fiber release depends on:

1.	Condition of material.

2.	Nature of disturbance.

3.	Amount of ACM.

1.3	ACM regulated under NESHAP is referred to as "regulated asbestos-containing material" (RACM) and includes:							31158

1.	Friable ACM.

2.	Category I nonfriable ACM that has become friable.

3.	Category I nonfriable ACM that has been or will be sanded, ground, cut or abraded.

4.	Category II nonfriable ACM that has already been or is likely to become crumbled, pulverized or reduced to powder.

A.	Threshold Amounts of Asbestos Containing Roofing Material	31158

1.A.1	Threshold amounts below which NESHAP does not regulate is as follows:

Single family homes or residential buildings with four or fewer units.

Roofing projects less than 160 SF regardless of removal method, type of material (Cat I or II) or its condition (friable or nonfriable). However recommend least destructive method of removal.

Roof cutter method for removing 5,580 SF of Category I roofing will create 160 SF of RACM (determined by EPA). Therefore removal of less than 5,580 SF by this method.

For any size, if slicing or other method that does not sand, grind, cut or abrade is used.

1.A.2	Category II (A/C Shingles). Not regulated by NESHAP when:	31158

Less than 160 SF regardless of the removal method.

Any area, if the material is not crumbled, pulverized, reduced to powder, or contaminated with RACM (from other ACM that has been crumbled, pulverized or reduced to powder).

B.	A/C Shingle Removal (Category II ACM Removal)		31158

1.B.1	A/C Shingles become regulated ACM (RACM) if the material has a high probability of becoming crumbled, pulverized or reduced to powder by the forces expected to act on the material in the course of demolition.

Merely breaking an A/C shingle that is not friable does not necessarily cause the material to become RACM.

C.	Cutting Verses Slicing and Manual Methods for Removal of Category I ACM	31158

1.C.1	Rotating blade cutters (RB) or other equipment that sand, grind or abrade roof materials are subject to NESHAP. The use of manual methods (using equipment such as axes, hatchets, or knives, spud bars, pry bars, and shovels but not power saws) or methods that slice, shear, or punch (using equipment such as a power slicer or power plow) does not constitute "cutting, sanding, grinding or abrading". Therefore they are not subject to regulation.

1.C.2	Power removers or power tear-off machines which are used to pry the material up from the deck after being cut is not regulated.

II.	Notification													31159

2.1	Notification for demolition is always required. Roof removal, when not a part of a demolition job, is "renovation" and notification is not required if the "Threshold Amounts" on page 2 of this summary are not exceeded.

2.2	Ten day advance notification except for emergencies if the notification requirement is applicable.

III.	Emission Control Practices									31159

A.	Requirements to Adequately Wet and Discharge No Visible Emission

3.A.1	Principal controls. Adequately wet, and asbestos wastes handled, collected and disposed of properly.

B.	Exemptions from Wetting Requirements				31159

3.B.1	Exceptions. Damage to building, equipment inside or safety hazard. Requires written approval from EPA.

3.B.2	Alternative control methods to wetting include:

Local exhaust ventilation system (capture dust). Other methods that have received the written approval of the EPA.

3.B.3	Wetting exemption. Air or roof surface temperature below freezing.

C.	Waste Collection and Handling							31159

3.C.1 &

3.C.2	Waste removed and handled in a manner which makes it not subject to NESHAP can be disposed of as non-asbestos waste.

3.C.2	When an RM cutter is used to cut Category I ACM, the damaged material from the cut (the sawdust or debris) is ACM subject to NESHAP if the thresholds are met or exceeded. However if the remainder of the roofing is free of sawdust and debris generated by cutting, it can be disposed of as non-asbestos waste.

3.C.3	When using a RB cutter to cut Category I ACM, the dust and debris resulting from cutting must be collected as soon as possible after the cutting and kept wet until placed in leak tight containers.

3.C.4	If the debris from cutting is not collected immediately, it should be lightly misted frequently to keep the material from drying and to prevent air-borne emissions.

3.C.5	The appearance of rough, jagged or damaged edges of roofing material, due to the use of an RB roof cutter, does not make the material "asbestos waste". The use of an encapsulant will ensure that the material need not be treated as asbestos containing waste material.

IV.	Waste Disposal												31160

A.	Disposal Requirements

4.A.1	As soon as practical, all collected dust and debris from cutting as well as any contaminated roofing squares, must be taken to a landfill. During loading and unloading, asbestos warning signs must be affixed to the vehicles.

B.	Waste Shipment Record									31160

4.B.1	A waste shipment record (WSR) must be maintained for each shipment of NESHAP regulated material.

V.	Training														31161

5.1	For roof removals subject to NESHAP at least one on-site supervisor trained in the provisions of NESHAP must be present during the removal of ACM. AHERA training courses, or other courses with similar content, are acceptable training.

END OF SECTION 13280 - ATTACHMENT B